aseXML Schema Change Request

PREPARED BY:	Wayne Lee

DOCUMENT REF:	CR60

VERSION:	0.5

DATE:	30-Mar -2017

Draft/Final	Final

Version Release History

| Version | Date | By | Changes |
| --- | --- | --- | --- |
| 0.1 | 27/01/2017 | Wayne Lee | Change proposal for POC B2B. |
| 0.2 | 24/02/2017 | Wayne Lee | Updated after January POC B2B consultation feedback and IEC response to the versions updated with feedback. |
| 0.3 | 24/02/2017 | Wayne Lee | Updated after ASWG walkthrough of 0.2. |
| 0.4 | 10/03/2017 | Wayne Lee | Updated after ASWG feedback of 0.3 Removed TransformerLocation from InstrumentTransformer. InstrumentTransformerType max reduced to 2 from 20. Modified enumerated values for SORDResponseCode Modify PrimaryVoltage to be 8 char max. |
| 0.5 | 30/03/2017 | Wayne Lee | Added ElectricityEnumerations.xsd file (non versioned against the schema). Moved enumerated lists for most new fields with ‘allowed values’ in procedure to new ElectricityEnumerations.xsd file. Added ElecIndexInvestigationCode as new enumerated list. Replaced IndexInvestigationCode simple type enumerated list with ElecIndexInvestigationCode for Electricity MeterDataVerifyRequest. |
| 0.6 | 24/04/2017 | Wayne Lee | Updated test outcomes and vote result. Finalised status. |
| 0.7 | 17/07/2017 | Wayne Lee | Change LifeSupport (under ElectricityServiceOrderDetails in Electricity_r36.xsd) to be optional. Change Meters (under RemoteServiceData in MeterDataManagement_r36.xsd) to be optional. |

Glossary

| Abbreviation | Description |
| --- | --- |

Contents

1	Change Proposal	5

1.1	Description of the proposed change	5

1.2	Reason for Change	7

1.3	Supplied Documents	7

1.3.1	Other	7

1.4	Baseline Schema	7

2	Approval Proposal	8

2.1	Proposed Change	8

2.1.1	Draft schema	8

2.1.2	Change log	8

2.1.3	Schema change description	12

2.1.4	Impact Summary	46

2.1.5	Developer Test	48

3	Proposal Assessment	48

3.1	Test	48

3.1.1	Test Platforms	48

3.1.2	Test Cases	48

3.1.3	Test Results	48

3.2	Conformance Report	48

4	Issue Register	48

4.1	Status of Issues	49

5	Resolution	49

5.1	ASWG Endorsement	49

# Change Proposal

This Change Proposal is to provide changes required to support the Power of Choice program:

- Enable multiple notified parties to be specified in the service order request transactions.

- Provide a one way notification type transaction to deliver details and progress information on service orders to multiple notified parties as a one way notification.

- Implement site access request transactions as customer and site detail transactions.

- Provide remote service request and response transactions as metering transactions.

- Provide notice of metering works transaction as a one way notification.

- Add life support, meter safety certificate, and coordination information to service order request transactions.

- Add email address to customer details notification.

- Modify the SwitchingServiceRequired element from Boolean to string.

- Replace IndexInvestigationCode enumerated list from common set to an electricity specific list.

- Update enumerations used in service order type and service order sub-type to reflect new Power of Choice requirements.

- Add PTPDataExchange freeform transaction to support unbounded peer to peer exchanges.

- Add PlannedInterruptionNotification transaction.

- Add MeterFaultAndIssueNotification transaction.

- Add new transaction groups to assign against the new transaction types.

## Description of the proposed change

The proposed changes are listed in the following table.

| Item# | Change Description | Change Type |
| --- | --- | --- |
|  | Modified Simple Type Added enumeration values to IndexInvestigationCode Added and removed enumeration values to ServiceOrderType Added and removed enumeration values to ServiceOrderSubType Added and removed enumeration values to SORDResponseCode Added enumeration values to TransactionGroup Added enumeration values to SupplyPhase Changed SwitchingServiceRequired from Boolean to string. Changed MeteringType to remove enumerated list. Modified Complex Type Transaction ElectricityMeter Product ElectricityMeterRegisterDetail ElectricityStandingData ElectricityMasterStandingData ElectricityServiceOrderDetails GasServiceOrderDetails ServiceOrderRequest ServiceOrderResponse CustomerDetailsNotification ElectricityServiceOrderNotificationData ElectricityServiceOrderType ElectricityVerifyMeterRequestData | Enhancement |
|  | New Simple Type SiteRequestReason EnergisationStatus GenerationType PrimaryVoltage InstrumentTransformerType DeviceSerialNumber DeviceLocation ControlEquipmentSerialNumber ControlEquipmentType ControlChannel InstrumentTransformerSerialNumber De-energisationReason RegisterIndexValue ResponsePayload RemoteServiceRequestCode UserDefinition RemoteServiceType ResponseFormat ServiceRequestID Latitude Longitude NoticeOfWorksID WorkType NotificationStatus NotificationNotes r36 EmailAddress AttachmentName AttachmentType ReasonForInter ReasonForNotice SupplyOff Duration MeterEquipmentType ElecIndexInvestigationCode New Complex Type SiteAccessRequest NetworkDevices NetworkDevice ControlEquipments ControlEquipment InstrumentTransformer InstrumentTransformers ConnectedMeters RemoteServiceData RemoteServiceResponseData UserDefData RemoteServiceResponse RemoteServiceRequest MeterSerialNumbers GeographicCoordinate NotifiedParties WorksDetail NotificationPayload RemovedMeteringEquipments RemovedMeteringEquipment NewEquipment NoticeOfMeteringWorks NotifiedParty PTPDataExchange P2PAttachment AttachmentList PlannedInterruptionNotification MeterFaultAndIssueNotification | New |
|  | New include file P2P_r36.xsd |  |

Table 1-1, Proposed Changes

## Reason for Change

Provide changes required to support the Power of Choice program.

## Supplied Documents

### Other

aseXML_r36.zip

## Baseline Schema

The schema used as a basis for this proposal is aseXML_r35.

# Approval Proposal

## Proposed Change

### Draft schema

Draft schema created as aseXML_r36.

### Change log

The following changes have been implemented in this draft:

| Chg # | Item # | Description of change | Filename |
| --- | --- | --- | --- |
| 1 | 1 | Updated schema namespace to ‘urn:aseXML:r36’. Updated Transactions schema to Transactions_r36.xsd Updated CustomerDetails schema to CustomerDetails_r36.xsd Updated Electricity schema to Electricity_r36.xsd Updated ElectricityMasterStandingData schema to ElectricityMasterStandingData_r36.xsd Updated MeterDataManagement schema to MeterDataManagement_r36.xsd Updated Common schema to Common_r36.xsd Updated OneWayNotification schema to OneWayNotification_r36.xsd Updated ServiceOrder schema to ServiceOrder_r36.xsd Updated Events schema to Events_r36.xsd Updated Gas schema to Gas_r36.xsd. Added Peer to Peer schema as P2P_r36.xsd Added non versioned Electricity specific enumerations lists as ElectricityEnumerations.xsd File version changed from r35 to r36. | aseXML_r36 |
| 2 | 1 | Added r36 release identifier in the Event schema. File version changed from r35 to r36. | Events_r36 |
|  |  | Added the following complex types for new transactions. SiteAccessRequest RemoteServiceResponse RemoteServiceRequest NoticeOfMeteringWorks NotifiedParty PlannedInterruptionNotification MeterFaultAndIssueNotification PTPDataExchange File version changed from r34 to r36. | Transactions_r36 |
|  |  | Added the following Complex Types for new transactions. SiteAccessRequest Modified the following Complex Types CustomerDetail Added EmailAddress as EmailAddress type. CustomerDetailsNotification (set to r36 version) Product Remove limit on Code element repeats. File version changed from r34 to r36. | CustomerDetails_r36.xsd |
|  |  | Added the following Simple Types DeviceSerialNumber ControlEquipmentSerialNumber ControlChannel InstrumentTransformerSerialNumber SwitchingServiceRequired type RegisterIndexValue type Added the following Complex Types NetworkDevices NetworkDevice ControlEquipments ControlEquipment InstrumentTransformer InstrumentTransformers ConnectedMeters type Modified the following Simple types ServiceOrderType Add enumerated values Remove redundant enumerated values ServiceOrderSubType Add enumerated values Remove redundant enumerated values SORDResponseCode Add enumerated values Remove redundant enumerated values SupplyPhase Add enumerated values MeteringType Remove enumerated list and set maximum length to 240 characters. Modified the following Complex types ElectricityMeter Add SupplyPhase Add GenerationType Add InstrumentTransformers Add GeneralSupply as YesNo type Add ControlEquipments for where associated with the meter. ElectricityServiceOrderDetails type (set to r36 version) Add MeterLicense Add De-energisationReason Add LifeSupport Add Co-ordinationRequired Modify SwitchingServiceRequired to be of type SwitchingServiceRequired as varchar(80) from boolean. ElectricityMeterRegisterDetail Add RegisterIndexValue as type RegisterIndexValue ElectricityVerifyMeterRequestData Modify InvestigationCode to be of type ElecIndexInvestigationCode Change the version attribute of versioned type to r36: ElectricityStandingData ServiceOrderRequestData ElectricityServiceOrderNotificationData ElectricityServiceOrderType ElectricityVerifyMeterRequestData File version changed from r35 to r36. | Electricity_r36.xsd |
|  |  | Modified the following Complex types ElectricityMasterStandingData Add EnergisationStatus Add PrimaryVoltage Add ControlEquipments Add NetworkDevices | ElectricityMasterStandingData_r36.xsd |
|  |  | Added the following Simple Types RemoteServiceRequestCode. RemoteServiceType. UserDefinition ResponseFormat. ServiceRequestID. Added the following Complex Types ResponsePayload. RemoteServiceData. RemoteServiceResponseData. UserDefData. MeterSerialNumbers. Added the following Complex Types for new transactions RemoteServiceResponse RemoteServiceRequest File version changed from r33 to r36. | MeterDataManagement_r36.xsd |
|  |  | Added the following Simple Types Latitude. Longitude Added the following Complex Types NotifiedParties. GeographicCoordinate Modified the following simple types Added enumeration values to IndexInvestigationCode Verify/Missing Register Require Estimate Data Meter Churn File version changed from r34 to r36. | Common_r36.xsd |
|  |  | Added the following Simple Types NoticeOfWorksID as string. NotificationNotes as string NotificationStatus as string Duration as string Added the following Complex Types WorksDetail NotificationPayload. RemovedMeteringEquipments RemovedMeteringEquipment NewEquipment Added the following Complex Types for new transactions NoticeOfMeteringWorks transaction. NotifiedParty transaction. PlannedInterruptionNotification MeterFaultAndIssueNotification File version changed from r33 to r36. | OneWayNotification_r36.xsd |
|  |  | Modified the following Complex types ServiceOrderRequest (set to r36 version) Add NotifiedParties Add Co-ordinatingContactDetail ServiceOrderResponse (set to r36 version) Change the version attribute of versioned type to r36: ServiceOrderRequest ServiceOrderResponse File version changed from r33 to r36. | ServiceOrder_r36.xsd |
|  |  | Added the following Simple Types EmailAddress as string type. File version changed from r15 to r36. | ClientInformation_r36.xsd |
|  |  | Modified the following Simple types TransactionGroup Add enumerated values | Header_r36.xsd |
|  |  | Added the following Simple types AttachmentName AttachmentType Added the following Complex types P2PAttachment AttachmentList Added the following Complex Types for new transactions PTPDataExchange | P2P_r36.xsd |
|  |  | Modified the following Complex types GasServiceOrderDetails (set to r36 version) File version changed from r33 to r36. | Gas_r36.xsd |
|  |  | Added the following Simple Types SiteRequestReason (max 40 string) ReasonForInter as string ReasonForNotice as string SupplyOff as string WorkType as string. EnergisationStatus PrimaryVoltage Max 8 string. GenerationType. Max 5 string. MeterEquipmentType as string. DeviceLocation as string. ControlEquipmentType InstrumentTransformerType. Max 2 string. De-energisationReason ElecIndexInvestigationCode | ElectricityEnumerations.xsd |

Table 2-1 Change Log

### Schema change description

#### aseXML_r36.xsd

- Updated schema namespace to ‘urn:aseXML:r36’.

- Updated Transactions schema to Transactions_r36.xsd

- Updated CustomerDetails schema to CustomerDetails_r36.xsd

- Updated Electricity schema to Electricity_r36.xsd

- Updated MeterDataManagement schema to MeterDataManagement_r36.xsd

- Updated Common schema to Common_r36.xsd

- Updated OneWayNotification schema to OneWayNotification_r36.xsd

- Updated ServiceOrder schema to ServiceOrder_r36.xsd

- Updated Events schema to Events_r36.xsd

- Updated Gas schema to Gas_r36.xsd

- Add P2P_r36.xsd

- Add ElectricityEnumerations.xsd

#### Events_r36.xsd

- Add r36 release identifier

<xsd:simpleType name="r36">

<xsd:annotation>

<xsd:documentation>Purpose - Release r36 identifier.</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="ReleaseIdentifier">

<xsd:enumeration value="r36"/>

</xsd:restriction>

</xsd:simpleType>

#### Transactions_r36.xsd

- Modify Transaction complex type:

- Add SiteAccessRequest element

- Add RemoteServiceResponse element

- Add RemoteServiceRequest element

- Add NoticeOfMeteringWorks element

- Add NotifiedParty element

<xsd:element name="SiteAccessRequest" type="SiteAccessRequest"/>

…

<xsd:element name="RemoteServiceRequest" type="RemoteServiceRequest"/>

<xsd:element name="RemoteServiceResponse" type="RemoteServiceResponse"/>

…

<xsd:element name="NoticeOfMeteringWorks" type="NoticeOfMeteringWorks"/>

<xsd:element name="NotifiedParty" type="NotifiedParty"/>

<xsd:element name="PlannedInterruptionNotification" type="PlannedInterruptionNotification"/>

<xsd:element name="MeterFaultAndIssueNotification" type="MeterFaultAndIssueNotification"/>

…

<xsd:element name="PTPDataExchange" type="PTPDataExchange"/>

#### CustomerDetails_r36.xsd

- Add SiteAccessRequest complex type as new transaction.

<xsd:complexType name="SiteAccessRequest">

<xsd:annotation>

<xsd:documentation>NEM - B2B Electricity: Transaction Group:  SITE; Purpose: Request site access - National Electricity B2B Process - Tranche 1 Build Pack; VicGas:  Not Used.			</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="NMI" type="NMI"/>

<xsd:element name="Reason" type="SiteRequestReason"/>

<xsd:element name="SpecialNotes" type="SpecialComments" minOccurs="0"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

- Modify CustomerDetail complex type

  - Add EmailAddress as type EmailAddress

<xsd:complexType name="CustomerDetail">

<xsd:annotation>

<xsd:documentation>Purpose - Defines the customer details for notification</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:choice>

<xsd:element name="PersonName" type="PersonName"/>

<xsd:sequence>

<xsd:element name="BusinessName" type="BusinessName"/>

<xsd:element name="ContactName" type="PersonName" minOccurs="0" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:choice>

<xsd:element name="PostalAddress" type="Address" minOccurs="0"/>

<xsd:element name="PhoneNumber" type="AustralianPhoneNumber" minOccurs="0" maxOccurs="unbounded"/>

<xsd:element name="EmailAddress" type="EmailAddress" minOccurs="0" maxOccurs="unbounded"/>

<!-- xsd:element name="SpecialCondition" type="SpecialCondition" minOccurs="0"/  insert after phone number -->

</xsd:sequence>

</xsd:complexType>

- Change the version attribute of versioned type to r36:

- CutomerDetailsNotification  complex type

Change from: xsd:attribute name="version" type="r32" use="optional" default="r32"/>

Change to: <xsd:attribute name="version" type="r36" use="optional" default="r36"/>

- Modify Product complex type

  - Remove limit on occurrances of Code element

<xsd:complexType name="Product">

<xsd:sequence>

<xsd:element name="Code" maxOccurs="unbounded">

<xsd:simpleType>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="10"/>

</xsd:restriction>

</xsd:simpleType>

</xsd:element>

</xsd:sequence>

</xsd:complexType>

#### Electricity_r36.xsd

- Add DeviceSerialNumber simple type

<xsd:simpleType name="DeviceSerialNumber">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="12"/>

</xsd:restriction>

</xsd:simpleType>

- Add ControlEquipmentSerialNumber  simple type

<xsd:simpleType name="ControlEquipmentSerialNumber">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="12"/>

</xsd:restriction>

</xsd:simpleType>

- Add ControlChannel simple type

<xsd:simpleType name="ControlChannel">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="12"/>

</xsd:restriction>

</xsd:simpleType>

- Add InstrumentTransformerSerialNumber  simple type

<xsd:simpleType name="InstrumentTransformerSerialNumber">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="12"/>

</xsd:restriction>

</xsd:simpleType>

- Add SwitchingServiceRequired simple type

<xsd:simpleType name="SwitchingServiceRequired">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="80"/>

</xsd:restriction>

</xsd:simpleType>

- Add RegisterIndexValue simple type

<xsd:simpleType name="RegisterIndexValue">

<xsd:annotation>

<xsd:documentation>

Purpose - Meter Register Index value as standalone.

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="15"/>

</xsd:restriction>

</xsd:simpleType>

- Add NetworkDevices complex type.

<xsd:complexType name="NetworkDevices">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="NetworkDevice" type="NetworkDevice" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Add NetworkDevice complex type.

<xsd:complexType name="NetworkDevice">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure network device detail.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="NetworkDeviceNumber" type="DeviceSerialNumber" minOccurs="0"/>

<xsd:element name="NetworkDeviceLocation" type="DeviceLocation" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add ControlEquipments complex type.

<xsd:complexType name="ControlEquipments">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="ControlEquipment" type="ControlEquipment" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Add ControlEquipment complex type.

<xsd:complexType name="ControlEquipment">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Control Equipment detail.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="ControlEquipmentNumber" type="ControlEquipmentSerialNumber"  minOccurs="0"/>

<xsd:element name="ControlEquipmentType" type="ControlEquipmentType"  minOccurs="0"/>

<xsd:element name="ControlChannel" type="ControlChannel"  minOccurs="0"/>

<xsd:element name="ConnectedMeters" type="ConnectedMeters" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add InstrumentTransformers complex type.

<xsd:complexType name="InstrumentTransformers">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="InstrumentTransformer" type="InstrumentTransformer" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Add InstrumentTransformer complex type.

<xsd:complexType name="InstrumentTransformer">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Control Equipment detail.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="TransformerNumber" type="InstrumentTransformerSerialNumber" minOccurs="0"/>

<xsd:element name="TransformerType" type="InstrumentTransformerType" minOccurs="0"/>

<xsd:element name="TransformerRatio" type="MeterTransformerRatio" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add ConnectedMeters complex type.

<xsd:complexType name="ConnectedMeters">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Control Equipment detail.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="SerialNumber" type="MeterSerialNumber"  minOccurs="0" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Modify ElectricityMeter complex type.

  - Add SupplyPhase element

  - Add GenerationType element

  - Add InstrumentTransformers element

  - Add GeneralSupply element

  - Add ControlEquipments element

<xsd:complexType name="ElectricityMeter">

<xsd:annotation>

<xsd:documentation>

Purpose - container for electricity meter information

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="SerialNumber" type="MeterSerialNumber" nillable="true" minOccurs="0"/>

<xsd:element name="NextScheduledReadDate" type="xsd:date" nillable="true" minOccurs="0"/>

<xsd:element name="Location" type="MeterLocation" nillable="true" minOccurs="0"/>

<xsd:element name="Hazard" type="MeterHazard" nillable="true" minOccurs="0"/>

<xsd:element name="InstallationTypeCode" type="MeterInstallationTypeCode" nillable="true" minOccurs="0"/>

<xsd:element name="Route" type="MeterRoute" nillable="true" minOccurs="0"/>

<xsd:element name="Use" type="MeterUse" nillable="true" minOccurs="0"/>

<xsd:element name="Point" type="MeterPoint" nillable="true" minOccurs="0"/>

<xsd:element name="Manufacturer" type="MeterManufacturer" nillable="true" minOccurs="0"/>

<xsd:element name="Model" type="MeterModel" nillable="true" minOccurs="0"/>

<xsd:element name="TransformerLocation" type="MeterTransformerLocation" nillable="true" minOccurs="0"/>

<xsd:element name="TransformerType" type="MeterTransformerType" nillable="true" minOccurs="0"/>

<xsd:element name="TransformerRatio" type="MeterTransformerRatio" nillable="true" minOccurs="0"/>

<xsd:element name="Constant" type="MeterConstant" nillable="true" minOccurs="0"/>

<xsd:element name="LastTestDate" type="xsd:date" nillable="true" minOccurs="0"/>

<xsd:element name="NextTestDate" type="xsd:date" nillable="true" minOccurs="0"/>

<xsd:element name="TestResultAccuracy" type="MeterTestResultAccuracy" nillable="true" minOccurs="0"/>

<xsd:element name="TestResultNotes" type="MeterTestResultNotes" nillable="true" minOccurs="0"/>

<xsd:element name="TestPerformedBy" type="MeterTestPerformedBy" nillable="true" minOccurs="0"/>

<xsd:element name="MeasurementType" type="MeterMeasurementType" nillable="true" minOccurs="0"/>

<xsd:element name="ReadTypeCode" type="MeterReadTypeCode" nillable="true" minOccurs="0"/>

<xsd:element name="RemotePhoneNumber" type="MeterRemotePhoneNumber" nillable="true" minOccurs="0"/>

<xsd:element name="CommunicationsEquipmentType" type="MeterCommunicationsEquipmentType" nillable="true" minOccurs="0"/>

<xsd:element name="CommunicationsProtocol" type="MeterCommunicationsProtocol" nillable="true" minOccurs="0"/>

<xsd:element name="DataConversion" type="MeterDataConversion" nillable="true" minOccurs="0"/>

<xsd:element name="DataValidations" type="MeterDataValidations" nillable="true" minOccurs="0"/>

<xsd:element name="Status" type="MeterStatusCode" minOccurs="0"/>

<xsd:element name="Program" type="MeterProgram" nillable="true" minOccurs="0"/>

<xsd:element name="AdditionalSiteInformation" type="MeterAdditionalSiteInformation" nillable="true" minOccurs="0"/>

<xsd:element name="EstimationInstructions" type="MeterEstimationInstructions" nillable="true" minOccurs="0"/>

<xsd:element name="AssetManagementPlan" type="MeterAssetManagementPlan" nillable="true" minOccurs="0"/>

<xsd:element name="CalibrationTables" type="MeterCalibrationTables" nillable="true" minOccurs="0"/>

<xsd:element name="UserAccessRights" type="MeterUserAccessRights" nillable="true" minOccurs="0"/>

<xsd:element name="Password" type="MeterPassword" nillable="true" minOccurs="0"/>

<xsd:element name="TestCalibrationProgram" type="MeterTestCalibrationProgram" nillable="true" minOccurs="0"/>

<xsd:element name="KeyCode" type="KeyCode" nillable="true" minOccurs="0"/>

<xsd:element name="CustomerFundedMeter" type="CustomerFundedMeter" nillable="true" minOccurs="0"/>

<xsd:element name="DisplayType" type="DisplayType" nillable="true" minOccurs="0"/>

<xsd:element name="SupplyPhase" type="SupplyPhase" minOccurs="0"/>

<xsd:element name="GenerationType" type="GenerationType" minOccurs="0"/>

<xsd:element name="GeneralSupply" type="YesNo" minOccurs="0"/>

<xsd:element name="InstrumentTransformers" type="InstrumentTransformers" minOccurs="0"/>

<xsd:element name="ControlEquipments" type="ControlEquipments" nillable="true" minOccurs="0"/>

<xsd:element name="RegisterConfiguration" type="ElectricityMeterRegisterConfiguration" nillable="true" minOccurs="0"/>

<xsd:element name="FromDate" type="xsd:date" minOccurs="0"/>

<xsd:element name="ToDate" type="xsd:date" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Modify ElectricityServiceOrderDetails type (set to r36 version)

  - Add MeterLicense

  - Add De-energisationReason

  - Add LifeSupport

  - Add Co-ordinationRequired

  - Modify SwitchingServiceRequired to use SwitchingServiceRequired type, changing to varchar(80) from boolean.

<xsd:complexType name="ElectricityServiceOrderDetails">

<xsd:annotation>

<xsd:documentation>Purpose - Defines the data type for new connection and meter additions and alterations

v36.1.  WL.  Change LifeSupport to be optional field.</xsd:documentation>

</xsd:annotation>

<xsd:complexContent>

<xsd:extension base="ServiceOrderRequestData">

<xsd:sequence>

<xsd:element name="CustomerConsultationRequired" type="xsd:boolean"/>

<xsd:element name="InstallationType" type="InstallationType" minOccurs="0"/>

<xsd:element name="SupplyPhase" type="SupplyPhase" minOccurs="0"/>

<xsd:element name="AverageDailyLoad" type="AveragedDailyLoad" minOccurs="0"/>

<xsd:element name="CustomerType" type="CustomerType" minOccurs="0"/>

<xsd:element name="MeteringType" type="MeteringType" minOccurs="0"/>

<xsd:element name="OffPeakRequirements" type="SpecialComments" minOccurs="0"/>

<xsd:element name="MaximumDemand" type="MeterDemand" minOccurs="0"/>

<xsd:element name="ServiceTime" type="ServiceTimeType" minOccurs="0"/>

<xsd:element name="SwitchingServiceRequired" type="SwitchingServiceRequired" minOccurs="0"/>

<xsd:element name="ConfirmedDe-energisation" type="xsd:boolean" minOccurs="0"/>

<xsd:element name="License" type="License" minOccurs="0"/>

<xsd:element name="MeterLicense" type="License" minOccurs="0"/>

<xsd:element name="De-energisationReason" type="De-energisationReason" minOccurs="0"/>

<xsd:element name="LifeSupport" type="YesNo" minOccurs="0"/>

<xsd:element name="Co-ordinationRequired" type="YesNo" minOccurs="0"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

- Modify ElectricityMeterRegisterDetail

- Add RegisterIndexValue element as type RegisterIndexValue

<xsd:complexType name="ElectricityMeterRegisterDetail">

<xsd:annotation>

<xsd:documentation>

Purpose - container for information about a register within an electricity meter

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="RegisterID" type="MeterRegisterIdentifier" minOccurs="0"/>

<xsd:element name="NetworkTariffCode" type="NetworkTariffCode" nillable="true" minOccurs="0"/>

<xsd:element name="NetworkAdditionalInformation" type="MeterNetworkAdditionalInformation" nillable="true" minOccurs="0"/>

<xsd:element name="UnitOfMeasure" type="MeterUnitOfMeasure" nillable="true" minOccurs="0"/>

<xsd:element name="TimeOfDay" type="MeterTimeOfDay" nillable="true" minOccurs="0"/>

<xsd:element name="Multiplier" type="MeterMultiplier" nillable="true" minOccurs="0"/>

<xsd:element name="DialFormat" type="MeterDialFormat" nillable="true" minOccurs="0"/>

<xsd:element name="Suffix" type="NMIDataStreamSuffix" nillable="true" minOccurs="0"/>

<xsd:element name="ControlledLoad" type="MeterControlledLoad" nillable="true" minOccurs="0"/>

<xsd:element name="ConsumptionType" type="MeterConsumptionType" nillable="true" minOccurs="0"/>

<xsd:element name="Demand1" type="MeterDemand" nillable="true" minOccurs="0"/>

<xsd:element name="Demand2" type="MeterDemand" nillable="true" minOccurs="0"/>

<xsd:element name="Status" type="MeterRegisterStatusCode" nillable="true" minOccurs="0"/>

<xsd:element name="DirectionIndicator" type="DirectionIndicator" nillable="true" minOccurs="0"/>

<xsd:element name="PreviousReading" type="ElectricityMeterReadData" nillable="true" minOccurs="0"/>

<xsd:element name="HighLowConsumption" type="HighLowConsumption" nillable="true" minOccurs="0"/>

<xsd:element name="RegisterIndexValue" type="RegisterIndexValue" nillable="true" minOccurs="0"/>

<xsd:element name="FromDate" type="xsd:date" minOccurs="0"/>

<xsd:element name="ToDate" type="xsd:date" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Modify ServiceOrderType to add enumerated values

- Supply Service Works

- Metering Service Works

- Modify ServiceOrderType  to remove redundant enumerated values

- New Connection

- Adds And Alts

- Allocate NMI

- Supply Abolishment

- Meter Investigation

- Metering Reconfiguration

<xsd:simpleType name="ServiceOrderType">

<xsd:annotation>

<xsd:documentation>Purpose - Defines a list of valid Service Order types supported by the particpants</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:enumeration value="Allocate NMI"/>

<xsd:enumeration value="New Connection"/>

<xsd:enumeration value="Re-energisation"/>

<xsd:enumeration value="De-energisation"/>

<xsd:enumeration value="Special Read"/>

<xsd:enumeration value="Adds And Alts"/>

<xsd:enumeration value="Meter Reconfiguration"/>

<xsd:enumeration value="Meter Investigation"/>

<xsd:enumeration value="Supply Abolishment"/>

<xsd:enumeration value="Miscellaneous"/>

<xsd:enumeration value="Metering Service Works"/>

<xsd:enumeration value="Supply Service Works"/>

</xsd:restriction>

</xsd:simpleType>

- Modify ServiceOrderSubType to add enumerated values

- Allocate NMI

- Change Timeswitch Settings

- Disconnect  at Pillar-Box Pit Or Pole-Top

- Establish Permanent Supply

- Establish Temporary In Permanent

- Establish Temporary Supply

- Local Meter Disconnection

- Meter Investigation-Inspect

- Meter Investigation-Test

- Meter Reconfiguration

- Move-in

- Physical Visit

- Recipient Discretion

- Remote

- Reseal Device

- Supply Abolishment

- Supply Alteration

- Tariff Change

- Temporary Isolation

- Temporary Isolation-Group Supply

- Modify ServiceOrderSubType to remove redundant enumeration values

- Change Controlled Load

- Change Tariff

- Change Timeswitch

- Inspect

- Install Hot Water

- Lab Test

- Meter Test

- Onsite Test

- Permanent

- Pillar-Box Pit Or Pole-Top

- Pillar-Box Pit Or Pole-Top (Non-Payment)

- Remove Fuse (Non-Payment)

- Sticker

- Tamper

- Temporary

- Temporary in Permanent

- Warning

<xsd:simpleType name="ServiceOrderSubType">

<xsd:annotation>

<xsd:documentation>Purpose - Defines a list of valid Service Order types supported by the particpants</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:enumeration value="Temporary"/>

<xsd:enumeration value="Temporary in Permanent"/>

<xsd:enumeration value="Permanent"/>

<xsd:enumeration value="Sticker Removal"/>

<xsd:enumeration value="New Reading Required"/>

<xsd:enumeration value="Warning"/>

<xsd:enumeration value="Remove Fuse (Non-Payment)"/>

<xsd:enumeration value="Pillar-Box Pit Or Pole-Top"/>

<xsd:enumeration value="Pillar-Box Pit Or Pole-Top (Non-Payment)"/>

<xsd:enumeration value="Sticker"/>

<xsd:enumeration value="Install Hot Water"/>

<xsd:enumeration value="Change Controlled Load"/>

<xsd:enumeration value="Change Timeswitch"/>

<xsd:enumeration value="Change Tariff"/>

<xsd:enumeration value="Tamper"/>

<xsd:enumeration value="Inspect"/>

<xsd:enumeration value="Onsite Test"/>

<xsd:enumeration value="Lab Test"/>

<xsd:enumeration value="Meter Test"/>

<xsd:enumeration value="After Disconnection For Non-Payment"/>

<xsd:enumeration value="Remove Fuse"/>

<xsd:enumeration value="Disconnect at Pillar-Box Pit Or Pole-Top"/>

<xsd:enumeration value="Install Controlled Load"/>

<xsd:enumeration value="Move Meter"/>

<xsd:enumeration value="Install Meter"/>

<xsd:enumeration value="Remove Meter"/>

<xsd:enumeration value="Exchange Meter"/>

<xsd:enumeration value="Check Read"/>

<xsd:enumeration value="Final Read"/>

<xsd:enumeration value="Allocate NMI"/>

<xsd:enumeration value="Establish Permanent Supply"/>

<xsd:enumeration value="Establish Temporary Supply"/>

<xsd:enumeration value="Establish Temporary In Permanent"/>

<xsd:enumeration value="Local Meter Disconnection"/>

<xsd:enumeration value="Meter Investigation-Inspect"/>

<xsd:enumeration value="Meter Investigation-Test"/>

<xsd:enumeration value="Meter Reconfiguration"/>

<xsd:enumeration value="Recipient Discretion"/>

<xsd:enumeration value="Remote"/>

<xsd:enumeration value="Supply Abolishment"/>

<xsd:enumeration value="Supply Alteration"/>

<xsd:enumeration value="Tariff Change"/>

<xsd:enumeration value="Temporary Isolation"/>

<xsd:enumeration value="Temporary Isolation-Group Supply"/>

<xsd:enumeration value="Change Timeswitch Settings"/>

<xsd:enumeration value="Reseal Device"/>

<xsd:enumeration value="Retrospective Move-in"/>

<xsd:enumeration value="Move-in"/>

<xsd:enumeration value="New Reading Required"/>

<xsd:enumeration value="Physical Visit"/>

</xsd:restriction>

</xsd:simpleType>

- Modify SORDResponseCode to add enumerated values

- Tariff Change Not Approved

- Inadequate infrastructure

- No Comms

- Life Support

- Metering not compatible with proposed Tariff Change

- Shared Supply Point

- Site Already Energised

- Request Submitted By Another Initiator

- Initiator Cancellation

- Recipient Cancellation

- Modify SORDResponseCode to remove enumerated values

- Retailer Cancellation

- Service Provider Cancellation

- Request Submitted By Another Retailer

<xsd:simpleType name="SORDResponseCode">

<xsd:annotation>

<xsd:documentation>Purpose - Defines a list of valid response code for different types of service orders</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:enumeration value="Customer On-Site"/>

<xsd:enumeration value="Customer Prevented"/>

<xsd:enumeration value="De-energisation Not Completed Due To A Re-energisation"/>

<xsd:enumeration value="Documentation Not Provided"/>

<xsd:enumeration value="Metering Problem"/>

<xsd:enumeration value="Meter Reading Only Undertaken Due To Prior Re-energisation"/>

<xsd:enumeration value="New Customer On-Site"/>

<xsd:enumeration value="No Supply"/>

<xsd:enumeration value="Other"/>

<xsd:enumeration value="Reading Problem"/>

<xsd:enumeration value="Request Submitted By Another Initiator"/>

<xsd:enumeration value="Initiator Cancellation"/>

<xsd:enumeration value="Sensitive Load"/>

<xsd:enumeration value="Recipient Cancellation"/>

<xsd:enumeration value="Unable To Access"/>

<xsd:enumeration value="Unknown Load"/>

<xsd:enumeration value="Unsafe"/>

<xsd:enumeration value="Tariff Change Not Approved"/>

<xsd:enumeration value="Inadequate infrastructure"/>

<xsd:enumeration value="No Comms"/>

<xsd:enumeration value="Life Support"/>

<xsd:enumeration value="Meter Not Retrieved"/>

<xsd:enumeration value="Metering not compatible with proposed Tariff Change"/>

<xsd:enumeration value="Shared Supply Point"/>

<xsd:enumeration value="Site Already Energised"/>

<xsd:enumeration value="Unknown Connection Status"/>

</xsd:restriction>

</xsd:simpleType>

- Modify SupplyPhase to add enumerated values

- Unknown

- Modify MeteringType to remove enumerated list

<xsd:simpleType name="MeteringType">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="240"/>

</xsd:restriction>

</xsd:simpleType>

Modify ElectricityStandingData  (set to r36 version)

Change from: xsd:attribute name="version" type="r35" use="optional" default="r35"/>

Change to: <xsd:attribute name="version" type="r36" use="optional" default="r36"/>

Modify ElectricityServiceOrderNotificationData (set to r36 version)

Change from: xsd:attribute name="version" type="r17" use="optional" default="r17"/>

Change to: <xsd:attribute name="version" type="r36" use="optional" default="r36"/>

Modify ElectricityServiceOrderType (set to r36 version)

Change from: xsd:attribute name="version" type="r19" use="optional" default="r19"/>

Change to: <xsd:attribute name="version" type="r36" use="optional" default="r36"/>

Modify ElectricityVerifyMeterRequestData (set to r36 version)

Modify InvestigationCode to use ElecIndexInvestigationCode simple type from IndexInvestigationCode simple type.

Change from: xsd:attribute name="version" type="r17" use="optional" default="r17"/>

Change to: <xsd:attribute name="version" type="r36" use="optional" default="r36"/>

<xsd:complexType name="ElectricityVerifyMeterRequestData">

<xsd:annotation>

<xsd:documentation>Purpose - used in MeterDataVerifyRequest transaction based on NMITransactionBase </xsd:documentation>

</xsd:annotation>

<xsd:complexContent>

<xsd:extension base="NMITransactionBase">

<xsd:sequence>

<xsd:element name="NMIStandingData" type="NMIStandingData"/>

<xsd:element name="InvestigationCode" type="ElecIndexInvestigationCode"/>

<xsd:element name="InvestigationDescription" type="SpecialComments"/>

<xsd:element name="RequestPeriod" type="OpenPeriod"/>

<xsd:element name="Current" type="ElectricityMeterReadData" minOccurs="0"/>

<xsd:element name="NMIConfiguration" type="NMIConfigurationType" minOccurs="0"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:extension>

</xsd:complexContent>

</xsd:complexType>

#### ElectricityMasterStandingData_r36.xsd

- Modify ElectricityMasterStandingData complex type:

- Add EnergisationStatus element

- Add PrimaryVoltage element

- Add ControlEquipments element

- Add NetworkDevices element

<xsd:complexType name="ElectricityMasterStandingData">

<xsd:annotation>

<xsd:documentation>

Purpose - container for non-repeating standing data associated with an electricity NMI

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="JurisdictionCode" type="JurisdictionCode" nillable="true" minOccurs="0"/>

<xsd:element name="NMIClassificationCode" type="NMIClassificationCode" nillable="true" minOccurs="0"/>

<xsd:element name="TransmissionNodeIdentifier" type="TransmissionNodeIdentifier" nillable="true" minOccurs="0"/>

<xsd:element name="DistributionLossFactorCode" type="DistributionLossFactorCode" nillable="true" minOccurs="0"/>

<xsd:element name="ParentEmbeddedNetworkIdentifier" type="EmbeddedNetworkIdentifier" nillable="true" minOccurs="0"/>

<xsd:element name="ChildEmbeddedNetworkIdentifier" type="EmbeddedNetworkIdentifier" nillable="true" minOccurs="0"/>

<xsd:element name="Address" type="AustralianPartialAddress" nillable="true" minOccurs="0"/>

<xsd:element name="Aggregate" type="YesNo" nillable="true" minOccurs="0"/>

<xsd:element name="Status" type="NMIStatusCode" nillable="true" minOccurs="0"/>

<xsd:element name="DistanceFromSubstation" type="DistanceFromSubstation" nillable="true" minOccurs="0"/>

<xsd:element name="VoltageType" type="VoltageType" nillable="true" minOccurs="0"/>

<xsd:element name="PoleNumber" type="PoleNumber" nillable="true" minOccurs="0"/>

<xsd:element name="AccessDetails" type="AccessDetail" nillable="true" minOccurs="0"/>

<xsd:element name="FeederClass" type="FeederClass" nillable="true" minOccurs="0"/>

<xsd:element name="CustomerClassificationCode" type="EMSDCustomerClassificationCode" nillable="true" minOccurs="0"/>

<xsd:element name="CustomerThresholdCode" type="EMSDCustomerThresholdCode" nillable="true" minOccurs="0"/>

<xsd:element name="ControlEquipments" type="ControlEquipments" nillable="true" minOccurs="0"/>

<xsd:element name="NetworkDevices" type="NetworkDevices" nillable="true" minOccurs="0"/>

<xsd:element name="EnergisationStatus" type="EnergisationStatus" nillable="true" minOccurs="0"/>

<xsd:element name="PrimaryVoltage" type="PrimaryVoltage" nillable="true" minOccurs="0"/>

<xsd:element name="FromDate" type="xsd:date" minOccurs="0"/>

<xsd:element name="ToDate" type="xsd:date" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

#### MeterDataManagement_r36.xsd

- Add ResponseFormat simple type.

<xsd:simpleType name="ResponseFormat">

<xsd:annotation>

<xsd:documentation>This element is used to define the Response payload format. eg CSV, XML, MDFF, BASE64</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="20"/>

</xsd:restriction>

</xsd:simpleType>

- Add RemoteServiceType simple type.

<xsd:simpleType name="RemoteServiceType">

<xsd:annotation>

<xsd:documentation>This element is used to define the RemoteService Type.</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="40"/>

</xsd:restriction>

</xsd:simpleType>

- Add RemoteServiceRequestCode simple type.

<xsd:simpleType name="RemoteServiceRequestCode">

<xsd:annotation>

<xsd:documentation>This element is used to define the RemoteServiceRequest code.</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="40"/>

</xsd:restriction>

</xsd:simpleType>

- Add UserDefinition simple type.

<xsd:simpleType name="UserDefinition">

<xsd:annotation>

<xsd:documentation>This element is used to define the User definitions as agreed between initiator and recipient.</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="240"/>

</xsd:restriction>

</xsd:simpleType>

- Add ServiceRequestID simple type.

<xsd:simpleType name="ServiceRequestID">

<xsd:annotation>

<xsd:documentation>This element is used to define the Remote service request ID.</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="15"/>

</xsd:restriction>

</xsd:simpleType>

- Add ResponsePayload complex type.

<xsd:complexType name="ResponsePayload">

<xsd:sequence>

<xsd:element name="RecordCount" type="RecordCount" minOccurs="0"/>

<xsd:element name="PayloadContent" type="xsd:anyType" nillable="true"/>

</xsd:sequence>

</xsd:complexType>

- Add MeterSerialNumbers complex type.

<xsd:complexType name="MeterSerialNumbers">

<xsd:annotation>

<xsd:documentation>Schema - RemoteService.  Collection of affected Meters</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="MeterSerialNumber" type="MeterSerialNumber" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Add UserDefData complex type.

<xsd:complexType name="UserDefData">

<xsd:annotation>

<xsd:documentation>Schema - RemoteService.  User definitions block</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="UserDef1" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef2" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef3" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef4" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef5" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef6" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef7" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef8" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef9" type="UserDefinition" minOccurs="0"/>

<xsd:element name="UserDef10" type="UserDefinition" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add RemoteServiceData complex type.

<xsd:complexType name="RemoteServiceData">

<xsd:annotation>

<xsd:documentation>Schema – RemoteService

r36.1  WL.    Change Meters element to be optional.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="RequestID" type="ServiceRequestID"/>

<xsd:element name="NMI" type="NMI"/>

<xsd:element name="Meters" type="MeterSerialNumbers" minOccurs="0"/>

<xsd:element name="ServiceType" type="RemoteServiceType"/>

<xsd:element name="RequestCode" type="RemoteServiceRequestCode"/>

<xsd:element name="ResponseFormat" type="ResponseFormat"/>

<xsd:element name="FromDateTime" type="xsd:dateTime" minOccurs="0"/>

<xsd:element name="ToDateTime" type="xsd:dateTime" minOccurs="0"/>

<xsd:element name="UserDef" type="UserDefData" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add RemoteServiceResponseData complex type.

<xsd:complexType name="RemoteServiceResponseData">

<xsd:annotation>

<xsd:documentation>Schema - ServiceOrder</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="ResponsePayload" type="ResponsePayload" minOccurs="0"/>

<xsd:element name="Event" type="Event" minOccurs="0"/>

<xsd:element name="Product" type="Product" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add RemoteServiceRequest complex type as new transaction

<xsd:complexType name="RemoteServiceRequest">

<xsd:annotation>

<xsd:documentation>Prior to commencing the use of the Remote Service Process the Initiator and Recipient must agree the scope of the service(s) and the format of the response to the service request.

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="RemoteServiceData" type="RemoteServiceData"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

- Add RemoteServiceResponse complex type as new transaction\

<xsd:complexType name="RemoteServiceResponse">

<xsd:annotation>

<xsd:documentation>Prior to commencing the use of the Remote Service Process the Initiator and Recipient must agree the scope of the service(s) and the format of the response to the service request.

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="RemoteServiceData" type="RemoteServiceData"/>

<xsd:element name="ResponseData" type="RemoteServiceResponseData"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

#### Common_r34.xsd

- Add Latitude simple type.

<xsd:simpleType name="Latitude">

<xsd:annotation>

<xsd:documentation>

Purpose - Provide geographic location coordinate.

Detail - Geographic latitude

The angular measurement North or South of the equator in decimal degrees (to 7 decimal places).   Angles South of the equator will be represented as negative values.   Eg -37.8886755

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:decimal">

<xsd:totalDigits value="9"/>

<xsd:fractionDigits value="7"/>

</xsd:restriction>

</xsd:simpleType>

- Add Longitude simple type

<xsd:simpleType name="Longitude">

<xsd:annotation>

<xsd:documentation>

Purpose – Provide geographic location coordinate.

Detail - Geographic longitude

The angular measurement East or West of the prime meridian in decimal degrees (to 7 decimal places).   Angles East of the Prime Meridian (eg Australia) will be represented as positive values.   Eg +145.1410361

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:decimal">

<xsd:totalDigits value="10"/>

<xsd:fractionDigits value="7"/>		</xsd:restriction>

</xsd:simpleType>

- Add complex type GeographicCoordinate

<xsd:complexType name="GeographicCoordinate">

<xsd:annotation>

<xsd:documentation>

Purpose - Coordinates specification</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="Latitude" type="Latitude"/>

<xsd:element name="Longitude" type="Longitude"/>

</xsd:sequence>

</xsd:complexType>

- Add NotifiedParties complex type.

<xsd:complexType name="NotifiedParties">

<xsd:annotation>

<xsd:documentation>

Purpose - List Notified parties</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="NotifiedPartyID" type="PartyIdentifier" minOccurs="0" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Modify IndexInvestigationCode simple type by adding enumeration values:

- Verify/Missing Registers

- Require Estimate Read

- Meter Churn

<xsd:simpleType name="IndexInvestigationCode">

<xsd:annotation>

<xsd:documentation>Schema - Gas</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:enumeration value="Confirm Reading For Vacant Site"/>

<xsd:enumeration value="Confirm Zero Consumption"/>

<xsd:enumeration value="Incomplete Data"/>

<xsd:enumeration value="Invalid MDFF Data"/>

<xsd:enumeration value="Invalid Standing Data"/>

<xsd:enumeration value="Missing Datastream"/>

<xsd:enumeration value="Require Actual Reading or Substitute"/>

<xsd:enumeration value="Require Final Substitute"/>

<xsd:enumeration value="Require Latest Version"/>

<xsd:enumeration value="Scheduled Reading Required"/>

<xsd:enumeration value="Service Order Reading Required"/>

<xsd:enumeration value="Verify High Reading"/>

<xsd:enumeration value="Verify Low Reading"/>

<xsd:enumeration value="Customer Away"/>

<xsd:enumeration value="Customer Query"/>

<xsd:enumeration value="Customer Read"/>

<xsd:enumeration value="High Account"/>

<xsd:enumeration value="Zero Consumption"/>

<xsd:enumeration value="Recipient Not Responsible For The NMI"/>

<xsd:enumeration value="Other"/>

<xsd:enumeration value="Cross Meter"/>

<xsd:enumeration value="MDL Out of Alignment"/>

<xsd:enumeration value="Verify/Missing Register"/>

<xsd:enumeration value="Require Estimate Data"/>

<xsd:enumeration value="Meter Churn"/>

</xsd:restriction>

</xsd:simpleType>

#### OneWayNotification_r33.xsd

- Add NoticeOfWorksID simple type as string.

<xsd:simpleType name="NoticeOfWorksID">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="12"/>

</xsd:restriction>

</xsd:simpleType>

- Add NotificationNotes simple type as string

<xsd:simpleType name="NotificationNotes">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="240"/>

</xsd:restriction>

</xsd:simpleType>

- Add NotificationStatus simple type as string

<xsd:simpleType name="NotificationStatus">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="30"/>

<xsd:enumeration value="SO Requested"/>

<xsd:enumeration value="SO Rejected"/>

<xsd:enumeration value="SO Completion"/>

<xsd:enumeration value="Accepted by Notified Party"/>

<xsd:enumeration value="Rejection by Notified Party"/>

<xsd:enumeration value="Notified Party Stopped"/>

</xsd:restriction>

</xsd:simpleType>

- Add Duration simple type as string

<xsd:simpleType name="Duration">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="5"/>

</xsd:restriction>

</xsd:simpleType>

- Add RemovedMeteringEquipments complex type

<xsd:complexType name="RemovedMeteringEquipments">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="RemovedMeteringEquipment" type="RemovedMeteringEquipment" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Add RemovedMeteringEquipment complex type

<xsd:complexType name="RemovedMeteringEquipment">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of removed equipment.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="RemovedEquipmentType" type="MeterEquipmentType"/>

<xsd:element name="MeteringEquipment" type="NMIStandingData"/>

</xsd:sequence>

</xsd:complexType>

- Add NewEquipment complex type

<xsd:complexType name="NewEquipment">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="InstalledMeterEquipment" type="ElectricityMeters" minOccurs="0"/>

<xsd:element name="InstalledNetworkDevices" type="NetworkDevices" minOccurs="0"/>

<xsd:element name="InstalledControlEquipment" type="NMIStandingData" minOccurs="0"/>

<xsd:element name="InstalledTransformers" type="ElectricityMeters" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add WorksDetail complex type

<xsd:complexType name="WorksDetail">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="WorkType" type="WorkType"/>

<xsd:element name="FieldWorkCompleteDateTime" type="xsd:dateTime"/>

<xsd:element name="TotalInstalledMeters" type="xsd:integer" minOccurs="0"/>

<xsd:element name="TotalInstalledNetworkDevices" type="xsd:integer" minOccurs="0"/>

<xsd:element name="TotalInstalledControlEquipment" type="xsd:integer" minOccurs="0"/>

<xsd:element name="TotalInstalledTransformers" type="xsd:integer" minOccurs="0"/>

<xsd:element name="TotalRemovedMeters" type="xsd:integer" minOccurs="0"/>

<xsd:element name="TotalRemovedOther" type="xsd:integer" minOccurs="0"/>

<xsd:element name="NewMeterEquipment" type="NewEquipment" minOccurs="0"/>

<xsd:element name="RemovedMeteringEquipments" type="RemovedMeteringEquipments" minOccurs="0"/>

</xsd:sequence>

</xsd:complexType>

- Add NotificationPayload complex type.

<xsd:complexType name="NotificationPayload">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:choice>

<xsd:element name="TransactionNotified" type="Transaction"/>

<xsd:element name="TransAckNotified" type="TransactionAcknowledgement"/>

<xsd:element name="MsgAckNotified" type="MessageAcknowledgement"/>

</xsd:choice>

</xsd:sequence>

</xsd:complexType>

- Add NoticeOfMeteringWorks complex type as new transaction.

<xsd:complexType name="NoticeOfMeteringWorks">

<xsd:sequence>

<xsd:element name="NoticeOfWorksID" type="NoticeOfWorksID"/>

<xsd:element name="NMIStandingData" type="NMIStandingData"/>

<xsd:element name="GeographicCoordinate" type="GeographicCoordinate" minOccurs="0"/>

<xsd:element name="MeterWorksDetail" type="WorksDetail"/>

<xsd:element name="Notes" type="NotificationNotes" minOccurs="0"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

- Add NotifiedParty complex type as new transaction.

<xsd:complexType name="NotifiedParty">

<xsd:sequence>

<xsd:element name="ServiceOrder" type="ServiceOrderHeader"/>

<xsd:element name="ServiceRequestor" type="PartyIdentifier"/>

<xsd:element name="ServiceProvider" type="PartyIdentifier"/>

<xsd:element name="ScheduledDate" type="xsd:date"/>

<xsd:element name="ActualDateTime" type="xsd:dateTime" minOccurs="0"/>

<xsd:element name="NotificationStatus" type="NotificationStatus"/>

<xsd:element name="RefTransaction" type="NotificationPayload"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

- Add PlannedInterruptionNotification complex type as new transaction.

<xsd:complexType name="PlannedInterruptionNotification">

<xsd:sequence>

<xsd:element name="NMI" type="NMI"/>

<xsd:element name="StartDate" type="xsd:date"/>

<xsd:element name="StartTime" type="xsd:time"/>

<xsd:element name="EndDate" type="xsd:date" minOccurs="0"/>

<xsd:element name="Duration" type="Duration"/

<xsd:element name="ReasonForInter" type="ReasonForInter" minOccurs="0"/>

<xsd:element name="Notes" type="NotificationNotes" minOccurs="0"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

- Add MeterFaultAndIssueNotification complex type as new transaction.

<xsd:complexType name="MeterFaultAndIssueNotification">

<xsd:sequence>

<xsd:element name="NMI" type="NMI"/>

<xsd:element name="DateIdentified" type="xsd:date"/>

<xsd:element name="StartDate" type="xsd:date" minOccurs="0"/>

<xsd:element name="StartTime" type="xsd:time"  minOccurs="0"/>

<xsd:element name="EndDate" type="xsd:date" minOccurs="0"/>

<xsd:element name="Duration" type="Duration" minOccurs="0"/>

<xsd:element name="SupplyOn" type="YesNo"/>

<xsd:element name="SupplyOff" type="SupplyOff" minOccurs="0"/>

<xsd:element name="Meters" type="ElectricityMeters"  minOccurs="0"/>

<xsd:element name="ReasonForNotice" type="ReasonForNotice"/>

<xsd:element name="Notes" type="NotificationNotes" minOccurs="0"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

#### ServiceOrder_r33.xsd

- Modify ServiceOrderRequest  complex type (set to r36 version)

  - Add NotifiedParties element

  - Add Co-ordinatingContactDetail element

<xsd:complexType name="ServiceOrderRequest">

<xsd:annotation>

<xsd:documentation>

Application - Service Order

TransactionExchange -

TransactionGroup - SORD

Priority - Medium

Purpose - Submit Service Order Request to the Service Provider

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="ServiceOrder" type="ServiceOrderHeader"/>

<xsd:element name="ServicePoint" type="ServicePoint" minOccurs="0"/>

<xsd:element name="ContactDetail" type="CustomerDetail" minOccurs="0"/>

<xsd:element name="CustomerDetail" type="CustomerDetail" minOccurs="0"/>

<xsd:element name="Co-ordinatingContactDetail" type="CustomerDetail" minOccurs="0"/>

<xsd:element name="AppointmentDetail" type="AppointmentDetail" minOccurs="0"/>

<xsd:element name="RequestData" type="ServiceOrderRequestData" minOccurs="0"/>

<xsd:element name="NotifiedParties" type="NotifiedParties" minOccurs="0"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

<xsd:attribute name="actionType" type="ActionType" default="New"/>

</xsd:complexType>

- Modify ServiceOrderResponse complex type (set to r36 version)

- Version change due to enumerations updates

<xsd:complexType name="ServiceOrderResponse">

<xsd:annotation>

<xsd:documentation>

Application - Service Order

TransactionExchange -

TransactionGroup - SORD

Priority - Medium

Purpose - Submit Service Order completion details to the Retailer

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="ServiceOrder" type="ServiceOrderHeader"/>

<xsd:element name="ContactDetail" type="CustomerDetail" minOccurs="0"/>

<xsd:element name="AppointmentDetail" type="AppointmentDetail" minOccurs="0"/>

<xsd:element name="NotificationData" type="ServiceOrderNotificationData" minOccurs="0"/>

<xsd:element name="Event" type="Event" minOccurs="0" maxOccurs="unbounded"/>

</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

<xsd:attribute name="responseType" type="ResponseType" default="Closure"/>

</xsd:complexType>

- Change the version attribute of versioned type to r36:

- ServiceOrderRequest  complex type

- ServiceOrderResponse  complex type

Change from: xsd:attribute name="version" type="r17" use="optional" default="r17"/>

Change to: <xsd:attribute name="version" type="r36" use="optional" default="r36"/>

#### ClientInformation_r36.xsd

- Add EmailAddress simple type (string).

<xsd:simpleType name="EmailAddress">

<xsd:annotation>

<xsd:documentation>

Purpose - Define email format.

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:pattern value="[^@]+@[^\.]+\..+"/>

</xsd:restriction>

</xsd:simpleType>

#### Header_r36.xsd

- Modify TransactionGroup simple type by adding enumeration values:

- MRSR

- OWNX

- NPNX

- PTPE

<xsd:simpleType name="TransactionGroup">

<xsd:annotation>

<xsd:documentation>

Purpose - Provide the transaction group to which all the contained transactions or transaction acknowledgments belong

Detail - The target application is at liberty to reject any transactions within the message that do not belong to the stated TransactionGroup. Where only message acknowledgements are carried, a transaction group of "MSGS" should be used.

The following groups are B2B process related:

FLTS - Faults and Outages

SORD - Service order, planned works

NETB - Network billing

MTRD - Meter data

CUST - Customer related

NOTF - Notifications (broadcast)

MKTW - Wholesale market operations

HSMD - High Speed Monitoring system

OWNP - Own Way Notification

EMMS - Electricity Market Management System

ERFT-NSW-ACT Wholesale Transaction Type

IAIT-NSW-ACT Wholesale Transaction Type

MRSR  -  remote services request/response

OWNX  -  NOMW, PIN and MFN

NPNX  -  Notified Party transaction

PTPE  -  Peer to Peer bilateral exchange

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:enumeration value="CATS"/>

<xsd:enumeration value="MDMT"/>

<xsd:enumeration value="MSGS"/>

<xsd:enumeration value="NMID"/>

<xsd:enumeration value="FLTS"/>

<xsd:enumeration value="SORD"/>

<xsd:enumeration value="NETB"/>

<xsd:enumeration value="MTRD"/>

<xsd:enumeration value="CUST"/>

<xsd:enumeration value="NOTF"/>

<xsd:enumeration value="SITE"/>

<xsd:enumeration value="FLDW"/>

<xsd:enumeration value="OUTG"/>

<xsd:enumeration value="BAR"/>

<xsd:enumeration value="NMIF"/>

<xsd:enumeration value="MKTW"/>

<xsd:enumeration value="HSMD"/>

<xsd:enumeration value="OWNP"/>

<xsd:enumeration value="EMMS"/>

<xsd:enumeration value="ERFT"/>

<xsd:enumeration value="IAIT"/>

<xsd:enumeration value="MRSR"/>

<xsd:enumeration value="OWNX"/>

<xsd:enumeration value="NPNX"/>

<xsd:enumeration value="PTPE"/>

</xsd:restriction>

</xsd:simpleType>

#### P2P_r36.xsd

- Add AttachmentName simple type

<xsd:simpleType name="AttachmentName">

<xsd:restriction base="xsd:string">

</xsd:restriction>

</xsd:simpleType>

- Add AttachmentType simple type

<xsd:simpleType name="AttachmentType">

<xsd:restriction base="xsd:string">

<xsd:maxLength value="30"/>

</xsd:restriction>

</xsd:simpleType>

- Add P2PAttachment complex type

<xsd:complexType name="P2PAttachment">

<xsd:annotation>

<xsd:documentation>Purpose - Define the attributes for each attachment.</xsd:documentation>

</xsd:annotation>

<xsd:attribute name="type" type="AttachmentType"/>

<xsd:attribute name="name" type="AttachmentName"/>

</xsd:complexType>

- Add AttachmentList complex type

<xsd:complexType name="AttachmentList">

<xsd:annotation>

<xsd:documentation>Purpose - Define the structure of Work details.</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="Attachment" type="P2PAttachment" minOccurs="0" maxOccurs="unbounded"/>

</xsd:sequence>

</xsd:complexType>

- Add PTPDataExchange complex type as new transaction.

<xsd:complexType name="PTPDataExchange">

<xsd:sequence>

<xsd:element name="FreeFormData" type="xsd:anyType" nillable="true"/>

<xsd:element name="AttachmentList" type="AttachmentList" minOccurs="0"/>			</xsd:sequence>

<xsd:attribute name="version" type="r36" use="optional" default="r36"/>

</xsd:complexType>

#### Gas_r36.xsd

- Change the version attribute of versioned type to r36:

- GasServiceOrderDetails complex type

Change from: xsd:attribute name="version" type="r34" use="optional" default="r34"/>

Change to: <xsd:attribute name="version" type="r36" use="optional" default="r36"/>

#### ElectricityEnumerations.xsd

- Add SiteRequestReason simple type (max 40 character string).

<xsd:simpleType name="SiteRequestReason">

<xsd:annotation>

<xsd:documentation>

Purpose - Define the fixed Reasons used to request site access details

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="40"/>

<xsd:enumeration value="New Retailer for site"/>

<xsd:enumeration value="Records old and need to be updated"/>

<xsd:enumeration value="No Access details on file for NMI"/>

<xsd:enumeration value="No Hazard Details on file for NMI"/>

<xsd:enumeration value="Site Visit Required"/>

<xsd:enumeration value="Other"/>

</xsd:restriction>

</xsd:simpleType>

- Add ReasonForInter simple type as string

<xsd:simpleType name="ReasonForInter">

<xsd:annotation>

<xsd:documentation>

Purpose - Define the fixed Reasons for interruption

Version 1.0 additions

- Meter Exchange - Individual

- Meter Exchange - Rollout

- Meter Replacement – Family Maintenance

- Meter Test

- Meter Fault Investigation

- Distribution Works

- Other

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="50"/>

<xsd:enumeration value="Meter Exchange - Individual"/>

<xsd:enumeration value="Meter Exchange - Rollout"/>

<xsd:enumeration value="Meter Replacement – Family Maintenance"/>

<xsd:enumeration value="Meter Test"/>

<xsd:enumeration value="Meter Fault Investigation"/>

<xsd:enumeration value="Distribution Works"/>								<xsd:enumeration value="Other"/>

</xsd:restriction>

</xsd:simpleType>

- Add ReasonForNotice simple type as string

<xsd:simpleType name="ReasonForNotice">

<xsd:annotation>

<xsd:documentation>

Purpose - Define the fixed Reasons for Notice

Version 1.0 additions

- Meter Family Failure

- Accuracy Failure

- Timeswitch/Controlled Load Failure

- Contactor Failure

- No Display

- Communication Failure

- Meter Verification

- Malfunction

- Area Event

- Metrology Threshold Breach

- Meter Bypassed

- Physical Damage

- Theft/Tampering

- Other

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="50"/>

<xsd:enumeration value="Meter Family Failure"/>

<xsd:enumeration value="Accuracy Failure"/>

<xsd:enumeration value="Timeswitch/Controlled Load Failure"/>

<xsd:enumeration value="Contactor Failure"/>

<xsd:enumeration value="No Display"/>

<xsd:enumeration value="Communication Failure"/>

<xsd:enumeration value="Meter Verification"/>

<xsd:enumeration value="Malfunction"/>

<xsd:enumeration value="Area Event"/>

<xsd:enumeration value="Metrology Threshold Breach"/>

<xsd:enumeration value="Meter Bypassed"/>

<xsd:enumeration value="Physical Damage"/>

<xsd:enumeration value="Theft/Tampering"/>

<xsd:enumeration value="Other"/>

</xsd:restriction>

</xsd:simpleType>

- Add SupplyOff simple type as string

<xsd:simpleType name="SupplyOff">

<xsd:annotation>

<xsd:documentation>

Purpose - Define the fixed Reasons for Notice

Version 1.0 additions

- Remove Fuse

- Remote

- Local Meter Disconnection

- Pillar-Box Pit Or Pole-Top

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="40"/>

<xsd:enumeration value="Remove Fuse"/>

<xsd:enumeration value="Remote"/>

<xsd:enumeration value="Local Meter Disconnection"/>

<xsd:enumeration value="Pillar-Box Pit Or Pole-Top"/> 						</xsd:restriction>

</xsd:simpleType>

- Add WorkType simple type as string.

<xsd:simpleType name="WorkType">

<xsd:annotation>

<xsd:documentation>

Purpose - Define the fixed work types for metering equipment works.

Version 1.0 additions

- Exchange Equipment

- Install Equipment

- Remove Equipment

- Relocate

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="50"/>

<xsd:enumeration value="Exchange Equipment"/>

<xsd:enumeration value="Install Equipment"/>

<xsd:enumeration value="Remove Equipment"/>

<xsd:enumeration value="Relocate"/>

</xsd:restriction>

</xsd:simpleType>

- Add EnergisationStatus simple type

<xsd:simpleType name="EnergisationStatus">

<xsd:annotation>

<xsd:documentation>

The energisation status of the metering installation

Version 1.0 additions

- Active

- Not Connected

- Deenergised Before Meter

- Deenergised At Meter

- Deenergised After Meter

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="30"/>

<xsd:enumeration value="Active"/>

<xsd:enumeration value="Not Connected"/>

<xsd:enumeration value="Deenergised Before Meter"/>

<xsd:enumeration value="Deenergised At Meter"/>

<xsd:enumeration value="Deenergised After Meter"/>

</xsd:restriction>

</xsd:simpleType>

- Add PrimaryVoltage simple type (Max 8 string).

<xsd:simpleType name="PrimaryVoltage">

<xsd:annotation>

<xsd:documentation>Indicates primary network voltage the metering installation is connected to

Version 1.0 additions

- 230V

- 400V

- 11KV

- 22KV

- 33KV

- 66KV

- 132KV

- Other HV

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="8"/>

<xsd:minLength value="1"/>

<xsd:enumeration value="230V"/>

<xsd:enumeration value="400V"/>

<xsd:enumeration value="11KV"/>

<xsd:enumeration value="22KV"/>

<xsd:enumeration value="33KV"/>

<xsd:enumeration value="66KV"/>

<xsd:enumeration value="132KV"/>

<xsd:enumeration value="Other HV"/>

</xsd:restriction>

</xsd:simpleType>

- Add GenerationType simple type (Max 5 string).

<xsd:simpleType name="GenerationType">

<xsd:annotation>

<xsd:documentation>

Indicates whether the meter is configured to measure the import of energy

Version 1.0 additions

- Net

- Gross

- None

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="5"/>

<xsd:enumeration value="Net"/>

<xsd:enumeration value="Gross"/>

<xsd:enumeration value="None"/>

</xsd:restriction>

</xsd:simpleType>

- Add MeterEquipmentType simple type (Max 25 string).

<xsd:simpleType name="MeterEquipmentType">

<xsd:annotation>

<xsd:documentation>

Indicates the meter equipment type

Version 1.0 additions

- Basic Meter

- Interval Meter

- Network Device

- Control Equipment

- Instrument Transformer

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="25"/>

<xsd:enumeration value="Basic Meter"/>

<xsd:enumeration value="Interval Meter"/>

<xsd:enumeration value="Network Device"/>

<xsd:enumeration value="Control Equipment"/>

<xsd:enumeration value="Instrument Transformer"/>

</xsd:restriction>

</xsd:simpleType>

</xsd:schema>

- Add DeviceLocation simple type

<xsd:simpleType name="DeviceLocation">

<xsd:annotation>

<xsd:documentation>

Indicates the network device location

Version 1.0 additions

- Before Meter

- After Meter

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="14"/>

<xsd:enumeration value="Before Meter"/>

<xsd:enumeration value="After Meter"/>

</xsd:restriction>

</xsd:simpleType>

- Add ControlEquipmentType simple type

<xsd:simpleType name="ControlEquipmentType">

<xsd:annotation>

<xsd:documentation>

Indicates the control equipmeht type

Version 1.0 additions

- Internal Relay

- External Relay

- Internal Time Switch

- External Time Switch

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="25"/>

<xsd:enumeration value="Internal Relay"/>

<xsd:enumeration value="External Relay"/>

<xsd:enumeration value="Internal Time Switch"/>

<xsd:enumeration value="External Time Switch"/>

</xsd:restriction>

</xsd:simpleType>

- Add InstrumentTransformerType simple type (Max 2 string).

<xsd:simpleType name="InstrumentTransformerType">

<xsd:annotation>

<xsd:documentation>Indicates instrument transformer type for the meter

Version 1.0 additions

- CT

- VT

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="2"/>

<xsd:enumeration value="CT"/>

<xsd:enumeration value="VT"/>

</xsd:restriction>

</xsd:simpleType>

- Add De-energisationReason simple type

<xsd:simpleType name="De-energisationReason">

<xsd:annotation>

<xsd:documentation>

Purpose - Define the fixed Reasons used to request De-energisation

Version 1.0 additions

- Customer Requested

- Move Out

- Non-Payment (DNP)

- Unauthorised Usage (DNI)

- Illegal Usage

- No Access

- Safety

- Defect

- Site Works

- Breach of Contract

- Other

</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:maxLength value="40"/>

<xsd:enumeration value="Customer Requested"/>

<xsd:enumeration value="Move Out"/>

<xsd:enumeration value="Non-Payment (DNP)"/>

<xsd:enumeration value="Unauthorised Usage (DNI)"/>

<xsd:enumeration value="Illegal Usage"/>

<xsd:enumeration value="No Access"/>

<xsd:enumeration value="Safety"/>

<xsd:enumeration value="Defect"/>

<xsd:enumeration value="Site Works"/>

<xsd:enumeration value="Breach of Contract"/>

<xsd:enumeration value="Other"/>

</xsd:restriction>

</xsd:simpleType>

- Add ElecIndexInvestigationCode simple type

<xsd:simpleType name="ElecIndexInvestigationCode">

<xsd:annotation>

<xsd:documentation>Schema - Elec</xsd:documentation>

</xsd:annotation>

<xsd:restriction base="xsd:string">

<xsd:enumeration value="Confirm Reading For Vacant Site"/>

<xsd:enumeration value="Confirm Zero Consumption"/>

<xsd:enumeration value="Incomplete Data"/>

<xsd:enumeration value="Invalid MDFF Data"/>

<xsd:enumeration value="Invalid Standing Data"/>

<xsd:enumeration value="Missing Datastream"/>

<xsd:enumeration value="Require Actual Reading or Substitute"/>

<xsd:enumeration value="Require Final Substitute"/>

<xsd:enumeration value="Scheduled Reading Required"/>

<xsd:enumeration value="Service Order Reading Required"/>

<xsd:enumeration value="Verify High Reading"/>

<xsd:enumeration value="Verify Low Reading"/>

<xsd:enumeration value="Other"/>

<xsd:enumeration value="Verify/Missing Register"/>

<xsd:enumeration value="Require Estimate Data"/>

<xsd:enumeration value="Meter Churn"/>

</xsd:restriction>

</xsd:simpleType>

### Impact Summary

This table identifies the files, transactions and versioned types that are potentially impacted as the result of these changes, where:

Modified types -  is a full list of types changed by this Change Request

Derived types – is a list of any types that are derived from a modified type, and are therefore also modified by default

Versioned types affected – is a list of all versioned types that will need to have the version attribute updated as a result of this Change Request

Transactions potentially affected – is a list of all transactions that contain a modified type, either directly or via a type substitution

Schema files affected – is a list of schema files that will be changed in some way as a result of this Change Request.

| Modified types | Derived types | Versioned types affected | Transactions potentially affected | Schema files affected |
| --- | --- | --- | --- | --- |
|  |  |  |  | aseXML_r34.xsd |
|  |  |  |  | Events_r34.xsd |
| ServiceOrderType ServiceOrderSubType ElectricityMeter ElectricityServiceOrderDetails ElectricityMeterRegisterDetail | ElectricityMeter ElectricityMeters | ElectricityStandingData ServiceOrderRequestData | NMIDiscoveryResponse NMIStandingDataResponse CATSChangeRequest CATSNotification CATSDataRequest ServiceOrderRequest ServiceOrderResponse AmendMeterRouteDetails AccountCreationNotification MeterReadInputNotification SpecialReadRequest SpecialReadResponse NMIStandingDataUpdateNotification CATSBulkDataRequest MeterReadingReferenceDataResponse ReportResponse | Electricity_r36.xsd |
| ElectricityMasterStandingData |  | ElectricityStandingData | MeterDataVerifyRequest MeterDataMissingNotification NMIStandingDataResponse NMIDiscoveryResponse CATSChangeRequest CATSNotification CATSDataRequest ReplicationNotification ReportResponse | ElectricityMasterStandingData_r36.xsd |
| ServiceOrderRequest ServiceOrderResponse |  |  | ServiceOrderRequest ServiceOrderResponse SpecialReadRequest SpecialReadResponse | ServiceOrder_r36.xsd |
| CustomerDetail |  | GasServiceOrderDetails | ServiceOrderRequest ServiceOrderResponse CustomerDetailsNotification | CustomerDetails_r36.xsd |

Table 2-2, Impact Summary

### Developer Test

#### Test Platforms

Development of modified schema files has been completed and tested.

#### Test Cases

- Basic regression tests with only absolutely required changes from r35 level. Eg mandatory LifeSupport element in ServiceOrderRequest transactions.

- Full inclusion of optional and required when available element.

- ControlEquipment attached to meter and wire connected to Meter cases.

- Notified party for transaction Ack, Message Nack, Service order request.

# Proposal Assessment

## Test

The ASWG ensures that all recommended parsers on relevant platforms can successfully validate the proposed schema.

### Test Platforms

Supplied samples have been tested using the following parsers:

MSXML 6.0 SP1

Xerces 2.2.1

Xerces 2.9.1

XMLSpy 2014

### Test Cases

NEMB2B_CustomerDetailsNotification_SiteVacant_r36.xml

NEMB2B_CustomerDetailsNotification_Update_BusinessName_r36.xm

NEMB2B_CustomerDetailsNotification_Update_r36.xml

NEMB2B_CustomerDetailsNotification_Update_Response_r36.xml

NEMB2B_CustomerDetailsReconciliation_r36.xml

NEMB2B_CustomerDetailsRequest_Other_r36.xml

NEMB2B_CustomerDetailsRequest_r36.xml

NEMB2B_MeterFaultAndIssueNotification_r36.xml

NEMB2B_PlannedInterruptionNotification_r36.xml

NEMB2B_PTPDataExchange_r36.xml

NEMB2B_RemoteServiceRequest_r36.xml

NEMB2B_RemoteServiceResponse_nonasexmlpayload_r36.xml

NEMB2B_ServiceOrderAppointmentNotification_r36.xml

NEMB2B_ServiceOrderRequest.Adds_n_Alts_r36.xml

NEMB2B_ServiceOrderRequestNewConnection_r36.xml

NEMB2B_ServiceOrderRequestNewConnection_Simple_r36.xml

NEMB2B_ServiceOrderResponse_C_r36.xml

NEMB2B_TransAck_Rejection_r36.xml

NEMMSATS_CustomerDetailsNotification_MovementType_r36.xml

NSWGAS_ServiceOrderRequest_MFX_example_-_JGN_r36.xml

NSWGAS_ServiceOrderRequest_MFX_example_-_WWT_r36.xml

VICGAS_ServiceOrderRequest(MeterFix)_01_r36.xml

VICGAS_ServiceOrderRequest(MeterFix)_02_r36.xml

VICGAS_ServiceOrderRequest(NewConnection)_r36.xml

### Test Results

Passed.

## Conformance Report

The ASWG completes the conformance report validating each proposed new schema file against the published aseXML guidelines.

| Schema Filename | Impacted by Item # | Conformance Details |
| --- | --- | --- |
| aseXML_r36 | 1,2,3 | <Conforms… or note non-conformance> |
| Events_r36 | 1,2,3 |  |
| Transactions_r36 | 2,3 |  |
| CustomerDetails_r36.xsd | 1 |  |
| Electricity_r36.xsd | 1 |  |
| ElectricityMasterStandingData_r36.xsd | 1 |  |
| MeterDataManagement_r36.xsd | 1 |  |
| Common_r36.xsd | 1 |  |
| OneWayNotification_r36.xsd | 2 |  |
| ServiceOrder_r36.xsd | 1,2 |  |
| ClientInformation_r36.xsd | 2 |  |
| Header_r36.xsd | 2,3 |  |
| P2P_r36.xsd | 3 |  |
| Gas_r36.xsd | 1 |  |
| ElectricityEnumerations.xsd | 2 |  |

Table 3-1, Change Proposal Conformance Details

# Issue Register

This section describes any issues that have arisen and any modifications that are made to the original proposal during the Change Process

## Status of Issues

| Issue# | Item# | Description and Discussion | Status | Resolution |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |

Table 4-1, Issues list

# Resolution

The ASWG votes for endorsement of the options identified in section 2, and the voting results are forwarded to AEMO for approval.  When 75% of those ASWG members who voted endorse a specific option, this represents an ASWG Recommendation for that option.  AEMO will not reject an ASWG Recommendation without first consulting with the ASWG.

## ASWG Endorsement

The results of the ASWG vote are as follows:

Date of Vote: 21/04/2017

| Option | # Votes | % Vote |
| --- | --- | --- |
| Option 1 (section 2.1) | 4 | 100% |
| Abstained |  |  |
| Total Members Present | 4 | 100% |

Table 5-1, ASWG Vote Results

# Footnotes

Change Type can be one of

- New

- Enhancement, or

- Bug Fix

Either ‘Open’ or ‘Closed’