## Slide 1: 5MS Joint Metering/Systems Focus Group
Monday, 12 November 2018
AEMO Office:
Level 2, 20 Bond Street, Sydney

## Slide 2: Agenda
NO |  | Time | AGENDA ITEM | Responsible
Preliminary Matters |  |  |  | 
1 | 10:00am - 10:15am | 9:30am – 9:40am | Welcome, introduction and apologies | Blaine Miner (AEMO)
Matters for Noting and Discussion |  |  |  | 
2 | 10:15am - 10:45am |  | Update on actions from 14 Sept meeting | Blaine Miner (AEMO)
3 | 10:45am - 11:20am |  | Transition to 5-minute meter data AEMO program schedule | Hamish McNeish (AEMO)
 | 11:20am - 11:30am |  | Break | 
4 | 11:30am - 1:00pm |  | Metering package #1 Consultation Topics | 
5 |  |  | Profiling 15 and 30-minute interval meters Controlled load 30-minute sample meters | David Ripper (AEMO)
6 |  |  | Alignment to B2B processes Register level meter data Non-energy meter data | Hamish McNeish & David Ripper (AEMO)
 | 1:00pm – 1:30pm |  | Lunch | 
7 | 1:30pm – 2:00pm |  | File size and communications capabilities | Hamish McNeish (AEMO)
8 | 2:00pm - 2:15pm |  | Potential removal of various RM reports | David Ripper (AEMO)
9 | 2:15pm - 2:30pm |  | Parking lot and other business | Blaine Miner (AEMO)
10 | 2:30pm – 2:45pm |  | Next steps | Blaine Miner (AEMO)

## Slide 3: Update on actions from 14 Sept meeting
Blaine Miner

## Slide 4: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
Modifying NEM12 format to support 5 minute meter reads | Interval length field to remain in the 200 record | Simply Energy raised the potential of moving the Interval Length field to the Header/100 record to allow for greater processing efficiency. Participants agreed that keeping the interval value in the 200 record would be preferred. | None | N/A | Interval length value to remain in the 200 record
Meter churn interval lengths | Intraday interval length changes should not be permitted. | Agreement that intraday interval length changes should not be permitted. | None | N/A | Intraday interval length changes will not be permitted in a meter churn event scenario.

## Slide 5: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
MDM meter read signage | Option 1: Use the first character of the data stream suffix (e.g. ‘E’ is Export+, ‘B’ is Import-) Option 2: New attribute to indicate whether the data stream (or register) is Import (B1) or Export (E1) or Signed (N1) in CNDS. | Option 1 preferred. New standing data / attribute not wanted. | None | N/A | MDFF: Signage to be derived based on the first character of the data stream suffix for interval meters and the direction indicator will be used for basic meters MDMF: Signage to be used as sent in the MDMF file
UOM validations | Option 1: Use MDFF Record 200 UOM to validate against ‘known’ UOM types. Option 2: New standing data field added to the CNDS table, and validate that the NEM12/13 content matches this. | Option 1 preferred. New standing data fields not wanted. UOM validations required. | None | N/A | UOM in the MDFF 200 record will be validated against known UOM types

## Slide 6: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
kWh meter read precision | AEMO’s systems to accept Wh, kWh and mWh meter reads. Stored values would be to 4 decimal places in kWh, rounding would occur if required. Other units of measure will be treated consistently e.g. vars. | 4 decimal place accuracy requirement mainly relevant to unmetered loads. AGL noted that the gas procedures provided guidance on how to round and when to round. | None | N/A | AEMO will round to 4 decimal places, consistent with the gas procedures Proposed rounding procedure has been provided to the joint focus group

## Slide 7: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
Converting 15 and 30-minute meter reads to 5 minute intervals | To implement a dynamic percentage allocation methodology, at the profile area level | Concerns raised that the proposed methodology may not be representative enough of non-5 minute meters, leading to material financial misallocations | No viable preferred alternative identified to date | AEMO and participants to continue to consider alternative methodologies | Pending
 |  | How would mixed meter types under a single NMI be treated under the proposed methodology? | None | N/A | No mixed metering installations have been identified

## Slide 8: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
MDFF vs MDMF | AEMO to transition to MDFF. Participants may use MDFF to send: Interval reads (E1, E2, B1, K1, Q1 etc) @ 5, 15 or 30-minute resolution and/or consumption reads for Basic meters. | Discussion regarding the benefits of AEMO becoming a B2B participant occurred e.g. allowing for more streamlining of processes and limits the changes to be made to MDP systems. Question regarding how MDFF could support existing AEMO MDM validation requirements was raised. | Participants to detail issues associated with supporting existing AEMO basic meter validations in MDFF. | Feedback from participants due 10 Oct | Pending
Missing meter data process | AEMO proposes to periodically run a RM11 report to inform MDP’s of missing meter reads | Automated AEMO initiated RM11 viewed favourably |  |  | AEMO to periodically run a RM11 report to inform MDP’s of missing meter reads

## Slide 9: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
Non-energy meter reads | AEMO to develop the ability to accept non-energy (e.g. Q and K) meter reads. | No concerns raised | None | N/A | AEMO to develop the ability to accept non-energy (e.g. Q and K) meter reads.
CATS NMI Datastream (CNDS) table maintenance | Option 1: Only settlement data streams are registered in CNDS Option 2: All data streams are registered in CNDS and validated, a new field would be required to indicate those to be used in settlement. Option 3: Use other existing attributes of CNDS, like Data stream Type, First character of suffix etc | Option 1 preferred | Consideration as to how CNDS maintenance can be made more efficient in light of the possible introduction of register level data streams | To be discussed at next JMSFG | Only settlement data streams are to be registered in the CNDS table

## Slide 10: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
Meter data storage where required standing data (i.e. NMI) does not exist. | ‘Parked’ meter data to be stored temporarily, for 3 days | Views varied regarding how long AEMO should store meter reads where required standing data does not exist, ranging from 3 days to 30 weeks. | Preferred number of days still not agreed | To be discussed at next JMSFG | Pending
File size and communications capabilities | To increase the current B2B and B2M 1 MB message content (uncompressed) limit to 10MBs. File size increase may be limited to Meter Read messages (MDFF and MDMF) due to performance considerations. Reason being that XML rich payloads (All other B2B and B2M transactions) may take too long to parse | Some MDPs advised that file sizes up to 10 MB were suitable, while still being able to handle the frequency, bandwidth and processing. DBs, MPs suggested that 10 MB could be too big for transaction processing and meeting SLAs. | Preferred file size not agreed | File size analysis to be completed by AEMO and participants by 21 Nov | Pending

## Slide 11: Topic Outcomes
Topic | AEMO Proposal | Discussion | Outstanding Issues | Next Steps | Outcome
Transition planning re 5MS implementation | Before 31 October 2020 – MDPs will need to aggregate 5 and 15 minute reads to 30 minute and provide in MDMF. Before 31 October 2020 – Participants and MDPs may choose to exchange new 5 and 15 minute data via B2B. From 31 October 2020 until 30 June 2021 – 5 and 15 minute reads received by AEMO will be aggregated by AEMO to 30 minutes. From 1 July 2021 AEMO will profile received 30 and 15 minute reads to 5 minute resolution. From 1 July 2022 AEMO will only accept retrospective reads via MDMF files. From 1 July 2023 AEMO will reject or ignore any received MDMF files | The Rules allows for the delivery of 5 minute meter data prior to 1 July 2021. Overall sentiment was that no participants would be ready for any 1 July 2020 production activities. AEMO has moved the start to 31 October 2020. A soft start of 31 March 2021 was suggested, to mitigate 1 July 2021 risks | Participants to provide information regarding transition activities and milestones by 12 Oct | To be discussed at next JMSFG | Pending

## Slide 12: Transition to 5-minute meter data
Hamish McNeish

## Slide 13: Topic Objectives
To communicate AEMO’s proposed high-level milestones in transitioning to MDFF.
To provide workshop attendees the opportunity to ask questions and make suggestions regarding this transition.
For actions to be assigned to AEMO and/or attendees regarding any outstanding matters.

## Slide 14: Implementing Five Minute Settlement
The Rule change requires the collection, storage and delivery of revenue metering data based on five-minute intervals for use in energy settlement, network and retail billing.
From a metering installation capability perspective, the rule requires:
Metering Installation | Record and provide 5-min meter data by
Type 1, 2, 3 and 7 | Commencement date of the rule
Type 4 (Trans. and Dist. Connection Point…) | Commencement date of the rule
All new and replacement metering installations, other than type 4A, installed from 1 December 2018 | 1 December 2022 at the latest
Type 4A metering installations installed from 1 December 2019 | 1 December 2022 at the latest
All other types 4, 5 and 6 meters already installed | Profiled to five-minute trading intervals by AEMO

## Slide 15: Current State – Delivery Format B2M
Business to Market protocols:
MDPs send Interval and Basic meter reads using the MDM File Format (MDMF).
Transaction Group of ‘MDMT’ is used to exchange B2M meter read data.
After meter read validations are performed by AEMO; validation results are delivered to MDPs via variety of acknowledgements as shown below:
  Message Acknowledgement - aseXML schema validations and file processing validations
  Transaction Acknowledgement - 1st level validations (only core validations listed):
    CSV content validation
    NMI & DataStream suffix validation
    MDP sending the reads matches the MDP in Standing Data
  Meter Data Response - 2nd level validations: Replacement read validations.

## Slide 16: Future State – Delivery Format B2B
AEMO is proposing to transition its current B2M message exchange to more closely align to relevant B2B processes.
AEMO is not proposing to become a B2B participant.
AEMO believes that unifying the data formats across the industry would result in both system and operational efficiencies.
AEMO proposes to decommission (after a transition period) the existing B2M meter data format.
AEMO is not proposing to use Provide Meter Data (PMD) or Verify Meter Data (VMD) processes for requesting missing meter data reads.
AEMO is planning to maintain any useful interactions with market participants (e.g. rejections equivalent to MDMF rejections)
AEMO would additionally propose to send participants scheduled RM11 reports to identify missing reads.

## Slide 17: AEMO program schedule
1 November 2020
  AEMO begins to accept MDFF files
1 November 2020 to 30 June 2021
  5 and 15 minute reads received by AEMO will be aggregated by AEMO to 30 minutes to support 30 minute settlements.
1 July 2021
  AEMO will profile received 15 and 30 minute reads to 5 minute resolution for settlement
1 July 2022
  AEMO will stop accepting new MDMF interval reads
  AEMO will continue to accept MDMF basic meter reads
TBC
  AEMO will decommission MDMF format

## Slide 18: Current Exchange Protocol

## Slide 19: Message Exchange Protocol – Post July 2022

## Slide 20: Topic Objectives - Recap
To communicate AEMO’s proposed high-level milestones in transitioning to MDFF.
To provide workshop attendees the opportunity to ask questions and make suggestions regarding this transition.
For actions to be assigned to AEMO and/or attendees regarding any outstanding matters.

## Slide 21: Profiling
David Ripper

## Slide 22: Topic Objectives
To share profiling methods considered by AEMO in converting 15 and 30-minute interval data to 5-minute resolution
  Including AEMO’s recommended methods.
To provide workshop attendees the opportunity to ask questions and make suggestions regarding these recommendations.
For actions to be assigned to AEMO and/or attendees regarding any outstanding matters.

## Slide 23: 15 and 30-minute Interval Metering Data Profiling
Between 1 November 2020 and June 2021 AEMO will aggregate 5 and 15-minute meter data to 30-minute for energy allocation
From 1 July 2021 AEMO will profile 15 and 30-minute metering data to 5-minute intervals.
From 1 July 2021 AEMO will profile 15 and 30-minute sample metering data to 5-minute intervals and apply that profile shape to controlled load reads for a Profile Area (PA) where CLP is to be prepared.

## Slide 24: Profiling Methods - 15 and 30-minute Non-Controlled Interval Meters
Method | Description | Complexity of Implementation (LNSP, etc) | Representative of 15/30min meters | Overall Comments
1 | 5-minute load profile- Apply 5-minute Load Profile to 1st and 2nd Tier 15 and 30-minute loads within PA (AEMO 5MS HLD). | Medium | Medium | Most representative option until critical mass exists to consider Option 2
2 | Residential and Business 5-minute metering profiles (Optional) - Apply separate Residential and Business profiles to residential and business customers respectively. Similar concept to CLP for a PA. | High | Medium/High | Type 1, 2, 3 and transmission type 4 will not be representative of residential and business customers. Need sufficient representative 5-minute metering installations for both residential and business customers per Profile Area for specific Residential and Business profiles to be viable.
3 | Simple Apportionment- 6 equal parts for 30-minute metering data or 3 equal parts for 15-minute metering data. | Low | Low (customer loads) Medium/High (controlled loads) | Not representative of associated customer (variable) loads. Good representation of controlled (constant) loads.

## Slide 25: Preparation of 5-minute Load Profile
Part 1 – Preparation of 5-minute load profile for a Profile Area
For each PA, the total energy for the wholesale boundary (sum of TNIs) is determined using five-minute metering data.
The energy associated with all non-wholesale boundary metering installations within the PA that have five-minute metering is summed, both for first-tier and second-tier connection points. This includes metering data associated with contestable Type 7 metering installations. Child connection points for embedded networks within a PA are ignored.
The energy associated with controlled load sample meters, with 15 or 30-minute metering data, is apportioned into 3 or 6 equal amounts respectively for each five-minute period. The five-minute controlled load sample meter energy is then summed to determine the ‘Controlled Load Profile’.
The energy associated with ‘non-sample’ or basic controlled load meters is summed, both for first-tier and second-tier connection points and then profiled by applying the ‘Controlled Load Profile’ calculated in Step 3.
The ’Five-minute load profile’ is then determined by subtracting the sum of all non-wholesale five-minute metering data (calculated in Step 2) and the sum of all controlled load five-minute metering data (calculated in Step 4, where applicable) from the PA’s wholesale boundary five-minute energy volume (calculated in Step 1).
Formula :
Five-minute load profile = ∑ Wholesale Boundary five-minute metered energy - ∑ Non-Wholesale Boundary five-minute metered energy (including contestable Type 7 metering installations) - ∑ Controlled Load five-minute energy

## Slide 26: Profiling Methods - 15 and 30-minute Non-Controlled Load Interval Meters
Part 2, Method 1 – Application of five-minute load profiles to support the calculation of NSLPs
The energy associated with all 15-minute interval meters is summed, both for first-tier and second-tier connection points.
The total of the 15-minute metering data (calculated in Step 1) is profiled using the ’Five-minute load profile’ shape (calculated in Step 5 of Part 1), which provides a five-minute representation of 15-minute metering data.
The energy associated with all 30-minute interval meters is summed, both for first-tier and second-tier connection points.
The total of the 30-minute metering data (calculated in Step 3) is profiled using the ’Five-minute load profile’ shape (calculated in Step 5 of Part 1), which provides a five-minute representation of 30-minute metering data.
The five-minute energy associated with 15 and 30-minute metering data (calculated in Steps 2 and 4) is subtracted from the “Five-minute Load Profile (calculated in Step 5 of Part 1), to derive the net system load profile (NSLP).
Formula :
NSLP = Five-minute Load Profile - ∑ Five-minute representation of 15-minute metering data - ∑ Five-minute representation of 30-minute metering data

## Slide 27: Profiling Option - 15 and 30-minute Non-Controlled Load Interval Meters
Part 3, Method 2 (Optional) – Residential and Business 5-minute profiles
For each applicable interval metering installation, source the Customer Classification Code (CCC) for the associated NMI for the period being profiled
  Where the CCC equals Null/Undefined, apply Part 2 (Option 1) methodology
  NMI Classification must equal ‘Large’ or ‘Small’
Sum the energy values of the 5-minute Residential meters by TI for each PA to determine the area’s ‘5-minute Residential profile’
Sum the energy values of the 5-minute Business meters by TI for each PA to determine the area’s ‘5-minute Business profile’
Apply the applicable ‘5-minute Residential profile’ to 15 and 30-minute meter reads in the PA where the NMI’s CCC is Residential
Apply the applicable ‘5-minute Business profile’ to the 15 and 30-minute meter reads in the PA where the NMI’s CCC is Business

## Slide 28: Profiling Methods - 15 and 30-minute Interval Meters
Part 4, Method 3 – Simple Apportionment
For each 15-minute meter read divide the recorded energy value into 3 equal parts.
For each 30-minute meter read divide the recorded energy value into 6 equal parts.

## Slide 29: Profiling Options - Controlled Load 15 and 30-minute sample meters
Simple Apportionment:
For each sample metering installation 15-minute interval period or 30-minute interval period described in clauses 3.9(b) and 3.9(c), respectively, of Metrology Procedure: Part A, divide the 15-minute energy value by 3 or the 30-minute energy value by 6 to produce a 5-minute energy value.
For each 15-minute or 30-minute period in (Step 1) apply the 5-minute energy value to each TI in the corresponding 15-minute interval period or 30-minute interval period to create 5-minute interval metering data for that sample metering installation.
The TI metering data produced in Step 2 will be used in the Profile Preparation Service – Controlled Load Process.
Method | Description | Complexity of Implementation | Representative of 15/30min meters | Overall Comments
1 | Simple Apportionment- 3 equal parts for 15-minute metering data or 6 equal parts for 30-minute metering data. | Low | Medium/High | Controlled loads are quite predictable and for the most part are either On or Off.
2 | Percentage Allocation based on a 5-minute profile Percentage allocation of 5-minute energy values for 15 or 30-minute periods. | High | Low | Any 5-minute profile includes variable loads, therefore the profile will not be representative of controlled load shapes

## Slide 30: Topic Objectives - Recap
To share profiling methods considered by AEMO in converting 15 and 30-minute interval data to 5-minute resolution
  Including AEMO’s recommended methods.
To provide workshop attendees the opportunity to ask questions and make suggestions regarding these recommendations.
For actions to be assigned to AEMO and/or attendees regarding any outstanding matters.

## Slide 31: Register Level Metering Data
David Ripper

## Slide 32: Topic Objectives
To share options considered by AEMO in transitioning from Net to Register Level meter data.
To provide workshop attendees the opportunity to ask questions and make suggestions regarding this transition.
For actions to be assigned to AEMO and/or attendees regarding any outstanding matters.

## Slide 33: Register Level Metering Data
AEMO Initial Position:
AEMO has the ability to accept register level (e.g. E and B) data streams and meter reads.
MDPs can either send register level or net values to AEMO
CNDS records must match NEM12 files
MDPs to determine associated register level data streams in CNDS table
Non-energy data streams can be included in the CNDS table as long as they are flagged appropriately so they are not used in Settlements

## Slide 34: Register Level Metering Data
Options Considered | Description | Constraints | Recommendation
MDPs specify data streams to be populated in CNDS table | MDP to raise CRs to change Net to Register level in CNDS or provide required data to AEMO to update CNDS via BCT | MDP effort to raise CRs. Design and implement change to BCT functionality. | Settlements data streams correctly mapped to CNDS – settlements integrity maintained.
Map CRI to CNDS | Validate the incoming MDFF reads against CRI and map CRI to CNDS | Standing data quality issues e.g. suffix in CRI Null, register exists but data stream doesn’t and vice versa, etc. | Not recommended – settlements integrity jeopardised.
Register to Data stream mapping derived from the MDFF 200 record | AEMO to interpret which data streams in CRI are to be populated in CNDS | Missing reads and configurations are determined from MDFF and not standing data Convoluted logic will be complicated when analysing data quality issues | Not recommended – settlements integrity jeopardised.
AEMO copies the suffixes in CRI to CNDS | AEMO to interpret which data streams in CRI are to be populated in CNDS | CRI Suffix could be Null Discrepancies between CRI and MDFF content | Not recommended – settlements integrity jeopardised.

## Slide 35: Register Level Metering Data
Change Request process
MDP initiates MSATS CRs to populate CNDS
Bulk Change Tool process
  MDPs to specify data stream changes required and provide them to AEMO
  AEMO initiates BCT
  Changes to occur over a period of time
  BCT responses would need to be accommodated

## Slide 36: Topic Objectives - Recap
To share options considered by AEMO in transitioning from Net to Register Level meter data.
To provide workshop attendees the opportunity to ask questions and make suggestions regarding this transition.
For actions to be assigned to AEMO and/or attendees regarding any outstanding matters.

## Slide 37: File size and communications capabilities
Hamish McNeish

## Slide 38: File size and communications capabilities
Objective: Increase maximum file (.xml) / message size to 10MB (both B2B & B2M)
AEMO’s approach:
  Identify impacted AEMO’s application, integration, infrastructure, storage and network components – Complete
  Perform end-to-end testing to validate the following – Planning in-progress
    Accept, parse and process the incoming files / messages (with increased file / message size)
    Generate outgoing files with new file size limits
    Impacts to database queries & storage
    Infrastructure constraints
    Network constraints
      Internal AEMO network and bandwidth constraints
      Participant-AEMO MarketNet and Internet bandwidth constraints
Options being evaluated:
  Option 1: Increase file size for all B2M and B2B message exchanges (i.e. all transaction groups)
  Option 2:
    Increase file size limits for MTRD & MDMT transaction groups (i.e. transactions with CSV payloads). Rationale: Parsing XML with heavy CSV payloads are not resource intensive
    Current file size limits apply to all other transaction groups

## Slide 39: File size and communications capabilities
Other considerations
  Unified file / message size limits for FTP and API protocol (vs) increased message size limits only for APIs
  Compressed payload for APIs
Next Steps:
AEMO will:
  Perform end-to-end internal tests to validate and deep-dive into the technical options
  Share test results / findings with the Focus Groups
  Work with Participants to identify their constraints
  Final recommendation: ~April 2019
Participant final confirmation expected during participant testing in AEMO’s Sandbox and Industry testing environments - ~November 2020

## Slide 40: Potential removal of various RM reports
David Ripper

## Slide 41: Potential removal of various RM reports
Potential retirement of some RM reports, due to lack of use
Report | Description | Usage
RM7 | MDP Data Delivery Report - Reports on Reads delivered by an MDP current as of a specific date and time (trans_startts) for a date range. | 20 Execution total, last run 2011 (1), 2005 (3), 2004 (12)
RM8 | Lists all profiles created and applied within a specified period. | 80 Execution total, last run 2017 (2), 2016 (2), 2015 (1), 2014 (2), 2013 (3), 2012 (3)
RM10 | Load Aggregation Error Report - Reports on processing errors (MSATS_Event_Log) in a settlement run. | 3 Execution total, last run 2004
RM12 | Wholesale Maximum Value Report - Reports on Wholesale (LR = POOL%) meter reads greater than a specified value. | 4 Execution total, last run 2006
RM14 | MDP Data Version Comparison Report allows the comparison of meter readings loaded on 2 separate date times for a single NMI. | 71 Execution total, last run 2014
RM15 | Multiple Versions Report is to provide information on the number of versions of metering data that have been supplied to the system by an MDP. | 94 Execution total, last run 2017 (2), 2016 (1), then 2014(3)
RM18 | Electricity Interval Data Report is to allow AEMO and Participants to retrieve all the metering data for a particular combination of TNI, FRMP, LR, and MDP. | 541 Execution total, last run 2017 (10), 2016 (50)
RM19 | Aggregated Actual vs Estimate Report - Counts of Actual Reads vs Estimated reads in a settlement run – Interval reads only – By TNI, FRMP, LR, MDP. | 15 Execution total, last run 2006 (1), 2004 (2)

## Slide 42: Parking Lot and General Business
Blaine Miner

## Slide 43: Next Steps
Blaine Miner

## Slide 44: Next Steps
Workshop outcomes and actions to be circulated
First Stage Metering Procedure Changes Package 1 Consultation published 31st October
Global Settlements Final Rule expected 6 December 2018
  Off-market unmetered supplies reminder

## Slide 45: Next Steps
Metering Package 2
  First Stage Consultation scheduled for April 2019
    Will consider both 5MS and Global Settlement Rules
  Procedures expected to be included:
    MSATS Procedures:
      Metering Data Management (MDM) Procedures
      MDM File Format and Load Process
      National Metering Identifier
      CATS Procedures Principles and Obligations
      Procedures for the Management of WIGS NMIS
    Metrology Procedure Part A
    Metrology Procedure Part B
    Exemption Procedure - Metering Provider Data Storage Requirements
    Service Level Procedure: Metering Data Provider Services
    Service Level Procedure: Metering Provider Services
    Retail Electricity Market Glossary and Framework

## Slide 46: Thank you for your attendance and participation!